EURO PROFILE CYLINDER

Measurement & Fitting Guide

(Featured in the website’s measuring guide video)

# Text boxes

X

Euro DOUBLE Cylinder

Euro SINGLE Cylinder (no keyhole inside property)

X

Euro Cylinder with Turn KNOB

Cylinder Removal

- Remove the screw which passes from the door edge into the cylinder at Point X.

- Turn the key to align the cam with the body.

- Slide the cylinder out to the key side.

If a Euro Cylinder with Turn Knob is fitted, there is no need to insert a key.  Just rotate the turn knob and slide the cylinder out to the turn knob side.

NB: If the cylinder is tight and does not move, you may have to loosen the door furniture and/or locking mechanism to facilitate the removal of the cylinder.

Cylinder Measurement

Using the diagrams to the left as a guide, take the measurements of A, B and C.  The sum of A plus B should always equal C.

Measurement of A = ………..………..

Measurement of B = …………..……..

Measurement of C = ..………………..

Ideally, the cylinder should fit flush with the door furniture/escutcheon. This is not always possible, but in all cases it should not project more than 3mm.

Cylinder Fit

- Align the cam with the cylinder’s body by turning the key.

- Slide the cylinder in from the key side.

- Replace the screw which passes from the door edge into the cylinder at Point X.

If in doubt, contact CIA’s qualified

Master Locksmiths for assistance.

T	023 9224 2449

F	023 9223 2730

E	locks@ciaalarms.co.uk

W	www.ciaalarms.co.uk

These instructions are for guidance only and CIA does not accept liability for any consequences resulting from their interpretation.

mm

X

© 2011 Christie Intruder Alarms Ltd, Security House, 212-218 London Road, Nr Portsmouth, Waterlooville, Hampshire PO7 7AJ

Christie Intruder Alarms Ltd is a

Master Locksmith Association

Approved Company

mm

mm